## Slide 1: Design methodology of freeze-thaw processes towards industrial manufacturing of induced pluripotent stem cells
M2
Yusuke Hayashi
iPS細胞の実生産に向けた凍結・解凍プロセスの設計手法
April 18, 2018
Lab seminar

## Slide 2: Background
Induced pluripotent stem (iPS) cells
  Potential to be differentiated into all tissue and organs.
  Attract much interest in disease modeling and personalized medicine.
  Standardization of manufacturing process is necessary.
Cell harvest
Initialization
Freeze-thaw
Cultivation
Differentiation

## Slide 3: Background
Freeze-thaw process
  It is required to transport and cryopreserve iPS cells.
  There are many freeze-thaw processes in manufacturing.
iPS cells are known to be vulnerable to freezing and thawing[1].
[1] C. J. Hunt, Transfusion Medicine and Hemotherapy (2011), [2] Y. Xu, et al., Arch. Biochem. Biophys. (2014),
[3] R. Li, et al., Tissue Engineering Part C Methods (2018), [4] Y. Nishimura et al. Neuroscience Research (2016)
Previous study
  Cryoprotective agent study[2]
  Experimental study[3,4]
In the freeze-thaw process, it is important to evaluate the impact of heat and mass transfer through the cell membrane.

## Slide 4: This study
Objective
Development of design methodology of freeze-thaw process for iPS cells considering heat and mass transfer
Modeling
Experiment
Simulation
Discussion and verification of results
Design methodology of freeze-thaw process

## Slide 5: Experiment (In the future)
Program freezer
Cryovial[1]
[1] Thermo Fisher Scientific Inc.
Program freezer (Freezing)
  Cooling rate : 1 K～3 K/min
  Lowest temp. : 193 K
Cryovial
  Made of polypropylene
  Diameter : 12 mm
  Height : 48 mm
Constant temperature water bath (Thawing)
  Temperature : 37℃
Water bath

## Slide 6: Freezing of cells
  Extracellular water is frozen.
  Water in a cell is transported by osmotic pressure.
  Depression of freezing point inside a cell occurs.
  The solute in a cell is frozen at the eutectic point.
Mechanism
Ice
Freezing completed!

## Slide 7: Modeling
Mass transfer
: Thickness of ice [m]
: Heat of fusion of ice [kJ kg-1]
: Membrane permeability [m s-1 Pa-1]
: Osmotic pressure difference [Pa]
Heat transfer

## Slide 8: Heat transfer simulation
Assumptions
  Freezer heat transfer : Natural convection
  Freezer temperature : 193 K (Constant)
  Initial vial temperature : 300 K
  Content of the vial : Water
R and kv are important design parameters.

## Slide 9: Heat transfer simulation
Freezer temperature
  Constant (193 K)
  ‒3 K/min (From 300 K)
Freezing procedure is also an important factor.

## Slide 10: Mass transfer simulation
Assumptions
  Cryoprotective agent : 10%DMSO
  Initial cell volume : 2.5010-15 [m3]
  Cell surface area : 8.8710-10 [m2]
  Permeable substance : Water
R and kv are important design parameters.

## Slide 11: Future plan
Experiment
  Survival rate after thawing
  Cell membrane permeability
  Effect of cryoprotective agent
Modeling & simulation
  Cell damage by osmotic pressure
  Intracellular ice formation
  Convection in the freezer
Evaluation of the process
  Survival rate
  Manufacturing cost

## Slide 12: Discussion
Other modeling & simulation
Other important design parameters
Evaluation method of the process